## Slide 1: SPU3 IP address auto config
April 10, 2018 rev C

## Slide 2: Problem – serial spu
Microcolor and Mercury serial SPU2/3 devices
  Completely interchangeable within any Microcolor or Mercury system with a serial interface.
  No regards to fountain assignment or press geography.
  Only required connection is RS422 serial cable to system computer.
  Customers can swap devices or order replacements without concern configuration. Must be correct P/N.
  Only real concern is version of SPU FW with very old Microcolor systems with RS232, no longer supported. All supported systems have very similar RS422 serial support.

## Slide 3: Spu3 ethernet
Adding Ethernet functionality to SPU3 now adds additional complexity to support of SPU.
SPU3 has always allowed Ethernet HTML communications for basic diagnostics. This required additional CAT5 cable to SPU3 location.
Now SPU3 Ethernet can host control the servos/sweep/water devices without serial support at system computer. (less cost)

## Slide 4: Support of spu3 ethernet
Ethernet interface requires configuration of SPU3 interface selections via HTML browser:
  Connection type (serial or Ethernet)
  SPU3 device IP address/port
  System computer IP address/port
Also critical to SPU3 Ethernet is the Mercury Server IP address within the system XML.
  The correct NIC IP address/port connecting the SPU3s
Without correct settings of these selections, device control from system computer will fail.

## Slide 5: Possible issues
HTML browser is required to setup SPU3, available in all Mercury systems but not Microcolor systems.
  Microcolor support must be serial only.
Issues may arise at many points of service
  FSE Installation of SPU3
  FSE Service of SPU3
  Customer’s service of SPU3
Wrong IP address/port in SPU3 selections will cause no communications or confused operations.

## Slide 6: How to make this requirement simple
Use the same technique as Netburner IPsetup application to find possible SPU3 on the connected network.
Compare the last known MAC addresses of the known working SPU3 configuration with today’s network topology.
Notify operator that a new device is seen on the network, do you want reconfigure SPUs?

## Slide 7: How to implement this feature?
Read the system XML for known SPU3 IP address, Mercury Server address/port, and fountain configuration. System XML file can be opened from any location or standard App Server location.
Scan the network for NB modules (same as IP setup application) and report back discovered SPU3 devices.
Compare discovered devices versus historical good configuration, report differences. Allow both serial and Ethernet control SPU3 devices, but all devices must be attached to PRESS NET App Server NIC via CAT5 cable.
Display the scanned data from network in tree view and use grid chart to display the network configuration of the SPU3 devices.
Individual SPU3 can be selected in the tree view and configuration data from network scan and matching IP address data from system XML.

## Slide 8: Implementation (cont’d)
Possibly automatically change the SPU3 settings of each new device to match the last known working configuration, under operator control.
Display of all of the configuration data in one place (MAC address and what fountains the SPU3 is connected to) should allow the SPU3 to correctly re-configured.
Application can be run from any computer connected to PRESS NET NIC, App Server computer or MFG computer,
Application should modify the following items on the SPU3: SPU3 control method, SPU3 unit IP address and SPU3 server IP address.
Saving the final data to a text file would be good to have.

## Slide 9: assumptions
SPU3 Ethernet will need a writable label containing:
  Blank area for SPU # attached to Mercury system.
  Blank area for IP address of this SPU3 device.
  MAC address to uniquely identify the SPU3 to each device discovered.
Application allows any SPU3 to be identified by lighting the Activity and Fault LEDs on unit to be reconfigured and operator confirms.

## Slide 10: Assumptions (cont’d)
New installations:
  Final test in MFG will test and write SPU # and IP address to each SPU3.
  FSE installing each SPU3 according to SPU # on the press layout drawing. System startup should be ‘plug-and-play’.

## Slide 11: Assumptions (cont’d)
SPU3 service
  If getting a new SPU3 to replace failed unit, customer or FSE installs the SPU3 and runs the SPU3 auto config app.
  App tells operator that devices are missing or added to the network, what new devices should be numbered (SPU# and IP address) and change the label if not correct. (according to the label on the SPU3 with matching MAC address.)
  If everyone provided the correct information, nothing should be changed. If there is incorrect information, then the app should be provide this correction.

## Slide 12
Thanks!